## Slide 1
TAO-MIR
Takashi MIYATA
Institute of Astronomy, University of Tokyo
S. Sako, T. Nakamura, K. Asano, M. Uchiyama,
T. Onaka, I. Sakon, H. Kataza, and TAO group

## Slide 2
Akari and Spitzer achieved excellent results in a number of astronomical fields
very high sensitivity / wide coverage of the sky
Groundbased observations at mid infrared are still important
- high spatial resolution
- monitoring capability
Mid infrared observations from the ground

## Slide 3
Recently time variations at mid-infrared wavelengths have been reported
quiescence
outburst
EX Lupi (FU Ori type, T Tauri star)
Abraham+ 2009
amorphous +
crystallized
silicate
amorphous
silicate
Key concepts of the TAOMIR
✓ T Tau stars, HAeBe
✓ AGB stars, Luminous Blue Variables, WR stars
✓ Comets....
10 20 30 40
10 20 30 40
Wavelength [um]
minimum
maximum
Onaka+ 2002

## Slide 4
Accurate monitoring at MIR
×Unstable sky condition
×Limited number of comparison stars
 Differential photometry cannot be applied.
c.f. optical / NIR wavelengths….
a lot of stars + wide filed of view
 Stars around a target object can be used
as a standard of comparison
Monitoring observations at MIR wavelength are difficult
Ground-based telescopes  accuracy of the photometry is a problem
Satellite telescopes  observing time is very competitive

## Slide 5
Not many stars in MIR sky
Filed of view of current MIR cameras : not so large (< 1arcmin)
 Only the target object is observed at once.
Schematics of the mid-infrared sky
Concept of the Field Stacker

## Slide 6
Concept of the Field Stacker
If we can take two (or more) discrete fields simultaneously.....
Differential photometric method can be applied
 improve precision and reliability dramatically

## Slide 7
Field Stacker
-- consists of two movable pick-up mirrors and a wedge shape mirror
-- picks up two discrete fields of the sky
-- brings into the instrument field of view
Simultaneous observation of two (or more) stars
To cold optics
From telescope
From telescope
Wedge shape mirror
Pick up mirror
Pick up mirror
Concept of the Field Stacker
Schematic drawing of the field stacker

## Slide 8
There are enough number of stars ??
Field of VIew | > 50mJy | > 300mJy
φ25’ | 55% | 51%
φ12.5’ | 48% | 39%
φ2.5’ | 23% | 13%
We counted # of MIR objects of Akari 9um survey data.
-- Akari 9um survey : ~7M objects with > 50mJy
( ~ 1sig1sec sensitivity of the TAOMIR)
Conceptual studies of the Field Stacker
You can use the Field Stacker
for ~ 30% of Akari 9um sources
Fraction of two or more objects in a field

## Slide 9
There are enough number of stars ??
Field of VIew | > 130mJy | > 1000mJy
φ25’ | 50% | 41%
φ12.5’ | 41% | 35%
φ2.5’ | 15% | 0.3%
You can use the Field Stacker
for ~20% of Akari 18um sources
Fraction of two or more objects in a field
At 18 micron
-- Akari 18um survey : ~1.6M objects with > 130mJy
( ~ 1sig1sec sensitivity of the TAOMIR)
Conceptual studies of the Field Stacker

## Slide 10
Time (sec)
0
20
40
60
80
100
1
1.1
0.9
1.2
0.8
Normalized Intensity
Time variations of star counts
Source A
Source B
A/B
Simultaneous observation improves the photometric accuracy?
Source A, B
A/B
Frequency (Hz)
0.01
0.05
0.1
0.4
1
10
100
0.1
Power
Power spectra of intensity
MIR images of two or more stars taken by COMICS
✓Variation of the intensity : 10% within 100 sec.
✓ Variations of two stars are synchronized
Simultaneous observations are effective
(at least within 1 arcmin)
Conceptual studies of the Field Stacker

## Slide 11
Field stacker for spectroscopy
The field stacker is also useful for spectroscopic observations.
Simultaneous observation enable us
accurate calibration of the atmospheric absorptions
especially for
around the ozone absorption band at 10 micron
Q-band or longer wavelength ranges

## Slide 12
✓ High spatial resolution
✓ Wide wavelength coverage
✓ Accurate monitoring
Covers 2-38 micron wavelength region ( over 4 octaves!)
Achieves diffraction limited spatial resolution
with the Field stacker
Key concepts of the TAOMIR

## Slide 13
Filters
Grisms
Filters
Grisms
Filters
Grisms
InSb 1k
    300K
    20K
Si:As ch.
Si:Sb ch.
InSb ch.
2-6μm
20-38μm
6-25μm
Field Stacker
Fore Optics
Slit
Flip-flop mirror
    5K
Si:As 1k
Si:Sb128
from Telescope
Desgin of the TAOMIR

## Slide 14
2m x 2mx 2m
Cold optics
(~20K)
4K GM
cryocooler
Desgin of the TAOMIR
↑ Cassegrain Focus
Pickup mirror
Pickup mirror
Wedge
Mirror
TAOMIR
Fore Optics
InSb Channel
Si:As Channel
Si:Sb Channel
All optics are reflective
 achieves good performances
two 4K cryocoolers (SHI)
Optics : 20K
Optics : 20K

## Slide 15
Parameters | Values |  |  | Notes
# of channels | 3 (Si:As / Si:Sb / InSb) |  |  | 
Detectors | Si:As 1k x 1k | Si:Sb 128 x 128 | InSb 1k x 1k | 
Wavelength coverage | 6-25um | 20-38um | 2-6um | 
Pixel scale | 0.1”/pix | 0.4”/pix | 0.1”/pix | @SUBARU telescope
Field of view | 2’ x 2’ or 1’x2’ x 2fields | 1’ x 1’ or 0.5’x1’ x 2fields | 2’ x 2’ or 1’x2’ x 2fields | @SUBARU telescope
Filters | max 16 filtes (6-25um) | max 16 filtes (20-38um) | max 16 filtes (2-6um) | 
Spectroscopy | R ~250 @Nband R~250 @Qband | R~100 @30um | R~300 @Lband (TBD) | w/ grism
Sensitivity (Img.) 1sig1sec | 40mJy @10um 130mJy @20um | (400mJy @30um?) |  | for point sources
Instrument size | 2m x 2m x 2m , < 2ton |  |  | 
Others | - A cold chopping unit is installed in fore-optics |  |  | 
TAOMIR : Specifications

## Slide 16
 | TAO-MIR | COMICS
Sensitivity | ~40mJy @10um 1s1s | ~30mJy @10um 1s1s
Spatial resolution | diffraction limited | diffraction limited
Filed of view | 120” x 120” or 60”x120”x2filed | ~ 40”x30”
Spectral resolution | R~250 @N-band R~250 @Q-band | R~250/2,500/10,000 @N-band R~2,500/5,000 @Q-band
Monitoring Accuracy | Good (w/ Field Stacker) | ---
MIR performances compared with COMICS
△
○
○
○
○
◎
◎
TAOMIR will add an unique function of
MIR monitoring observations to the SUBARU telescope
TAOMIR : Specifications
COMICS has advantages of
slightly higher sensitivity ( because TAOMIR has warm optics)
med/high resolution spectroscopic capabilities

## Slide 17
2m x 2mx 2m
2010
2011
2012
2013
2014......
Desgin and Development
Tests @ Mitaka
Observations
@ SUBARU
Observations
@ TAO
MAX38
TAO-MIR
TAO-MIR
first light
Atacama 1m telescope
Prototype instrument
TAOMIR : Schedule

## Slide 18
✓ TAOMIR is a new mid-infrared instrument
- wide wavelength coverage
- high spatial resolution
- accurate monitoring capabilities
✓ TAOMIR employs the field stacker system,
which picks up two discrete field
and brings them into the instrument filed.
 improves the precision and reliability
 accurate monitoring / spectroscopic observations
Summary of this talk
a new function to the SUBARU MIR observations!