## Slide 1: すばる次世代補償光学系に期待すること What we demand for the next generation Subaru AO - Kick off - 1. Current＋ 2. Next-generation
Masayuki Akiyama
(Astronomical Institute, Tohoku Univ.)
2010/09/10

## Slide 2: What do we demand for “current+” system
Sky coverage, larger is better
  For example, good correction with R=18mag TT-guide star with 60” distance, see later.
  NIR TT-guide star (TT-correction with AO-corrected stars) ?
Information on PSF at target position. Possible ? How reliable ?
  Especially for narrow fov observations. Accuracy with FWHM=0.10”+-0.02”, see later.

## Slide 3: Sky coverage limitation
Yes of course with NGS AO
  K-band SR~0.2 with R=13mag @ 30” (blue) ~6%@SXDS
  K-band SR~0.1 with R=15mag @ 30” (red) ~3%@SXDS
SXDS fov
~1000 X-ray sources are plotted with small dots

## Slide 4: Sky coverage limitation
Even with LGS AO (Keck LGS)
  K-band SR~0.2 with R=16mag @ 40” (blue) ~16%@SXDS
  K-band SR~0.1 with R=18mag @ 60” (red) ~58%@SXDS
SXDS fov
~1000 X-ray sources are plotted with small dots

## Slide 5
Feasible ? With what accuracy ?
No estimation necessary for point source spectroscopy.
Required accuracy is not so high for morphological studies of distant galaxies. Best fit morphological parameters do not severely depend on model PSF used.
Very high accuracy required for QSO host galaxy studies.
PSF estimation
MA+2008

## Slide 6: Next-generation general-purpose AO and Subaru’s originality
Targeting “cutting-edge + big size + general-purpose” = “costly and time-consuming” instrument ? Or chose either of one ?

## Slide 7: Next-generation general-purpose AO and Subaru’s originality
Unique AO instrument of ground-based 8-10m class telescope in the era of JWST(2014 launch)？
Competitive instrument even in the TMT(2018?) era ?
Wide field ? At least 5-10’ scale FoV. High-resolution version of NIR (prime-focus) wide-FoV camera.
  2.2’ x 2.2’ x 2 0.03” sampling with JWST NIRcam
High-spectral resolution ? R=3000 or higher with wide spectral coverage, at leaset one octove.
  R<1000-3000 0.1-0.2” sampling with JWST NIRspec
Shorter wavelength range ? High-spatial resolution observation in wavelength range 1um or shorter.

## Slide 8: NIRCam Design Features U of Arizona (M. Rieke) plus Lockheed ATC
NIRCam images the 0.6 to 5mm (1.7 - 5mm prime) range
  Dichroic used to split range into short (0.6-2.3mm) and long (2.4-5mm) sections
  Nyquist sampling at 2 and 4mm
  2.2 arc min x 4.4 arc min total field of view seen in two colors (40 MPixels)
  Coronagraphic capability for both short and long wavelengths
NIRCam is the wavefront sensor
  Must be fully
    redundant
  Dual filter/pupil
    wheels to
    accommodate
    WFS hardware
  Pupil imaging
    lens to check
    optical
    alignment

## Slide 9: NIRSpec
Multi-object dispersive spectrograph (MOS) for 1-5 µm
R~1000 or R~100 for MOS
MOS pixels ~0.2", and cover a ~ ~3’x3’ field
Capable of observing > 100 objects simultaneously.
Several fixed slits and an IFU (3”x3”) are also available with R as high as 3000.
Being built by the European Space Agency

## Slide 10: Directions, which do you want ?
Ultra-deep observation of individual target / 個別天体の深観測：
  Spectroscopy of very high-redshift galaxies: Lya emitter @ z=7
  High-SN, R~10,000 spectroscopy of QSOs：GP trough of z=6-7 QSOs
    Require higher SR
    = Extending shorter wavelength range
    With high sky coverage (targets are very rare)
Deep observation of multiple targets / 多天体の深観測：
  NIR spec. of red gals at intermediate z: Galaxies, AGNs @ z=1-3
    Moderate SR
    Wide FoV multi-object
Very-high spatial resolution of individual / 個別天体高空間分解能観測：
  High resolution observation of nearby galaxies: AGNs, stellar pops galaxies
    OPTICAL w.length range JWST will not reach,
    Higher spatial resolution than HST in optical
Direction 1
~ Keck-NGAO
~ Gemini-GEMS
Direction 2
Gemini-GEMS
Direction 3
Subaru-SCExAO？
Gemini-GPI ?

## Slide 11
With MCAO(Gemini GEMS)
  2’ fov covered with 3 TT guide stars brighter than R=18.5
  10% sky coverage at galactic pole with SR 0.6 in K-band
  3 R<18.5 stars within 60” = 15% @SXDS
  Degraded operation mode with 1 or 2 TTgs
Sky coverage limitation with next-gen.

## Slide 12: Direction 1, not 2：Gemini GEMS
GEMS is wide-field MCAO, but the expected performance is more closer to Keck NGAO (Direction 1), i.e. small FoV.

## Slide 13
With tomographic-AO (Keck NGAO)
  Requirements similar to Gemini GEMS?
Sky coverage limitation with next-gen.

## Slide 14: What SR do we want ?
Fraction of light within a slit varies with slit width. Different lines represent different SR ratio (shown with small numbers)
0.06” @ 8m K-band
0.24” slit
1/11
=1.3mag deeper
0.12” slit
1/44
=2.1mag deeper
0.80” slit
Seeing-limited

## Slide 15: What SR do we want ?
If background limited and point source, then, 3 mag deeper than current seeing limited observation with SR=0.7-0.8
0.06” @ 8m K-band
0.24” slit
1/11
=1.3mag deeper
~30-40%
0.12” slit
1/44
=2.1mag deeper
0.80” slit
60-80% encircled
0.8 mag deeper
SR~0.2
~0.4
~0.7

## Slide 16: BUT, the gain with higher SR is small for spec. of entire gals (extended obj.)
Narrower slits can be used for point sources with higher SR, BUT,,,
Galaxies at the intermediate redshifts (or at even higher redshifts) are significantly extended than diffraction limit, the gain with high SR will be smaller.
Of course, you can do spatially-resolved studies with high SR…
0.22” [OIII] in K
0.19” [OII] in H
0.17” [OII] in K
Bouwens et al. 2004, ApJ, 611, L1

## Slide 17: Spatially-resolved obs. of distant gals
Z=3 galaxy is observed with effectively 100pc (20-40mas) resolution thanks to gravitational lensing effect (Stark et al. 2008 Nature, 455, 755) 。
Clear rotation is detected for the first time with this very high spatial resolution.
Need to resolve 10km/s scale velocity structure, R~10,000 is necessary.
Considering required amount of light to achieve high-spatial and high-spectral resolution, this science case is for TMT ???
Major velocity structure within 1kpc (~0.1”)

## Slide 18: Target SR and required elements
AO36
AO188
AO1000
Direction１,3
Direction２

## Slide 19: What kind of inst do we need if dir２?
Wide FoV (d=8’) MOAO multi-object spec (only with long slits=no IFUs), R=3,000 double-beam spectrograph with zJHK coverage ?
Difficult to realize due to Rayleigh-scattering ?

## Slide 20: Summary (in J)
個別天体の深観測： HSCデータベースとの親和性は高い
  高赤方偏移の銀河の分光: Lya emitter @ z=7
  QSOの中分散(R~10,000)高SN分光：Gun-Peterson trough of z=6-7 QSOs
    より高いSR (0.6-0.7 @ K-band = 1,000 elements) で、
    =より短い波長 (~9000Aなど) で、
    高い sky coverage (>50%：GS:R=18mag,60”,1GS ) で。
多天体の深観測： MOIRCSなどの蓄積
  中赤方偏移の赤い銀河の分光観測: Galaxies, AGNs @ z=1-3
    そこそこのSR (0.1-0.3 @ K-band ~ 100 elements) で、
    広い視野(5-10’ scale)で多天体同時に。
個別天体の高空間分解能観測： わが道を行く？
  銀河中心の高空間分解能観測: AGN, stellar pops in local galaxies
    JWST の届かないより短い波長(<9000A)で。
    HSTで分解できなかったものを分解(SR=0.1@1um)。
Direction 1
~ Keck-NGAO
~ Gemini-GEMS
Direction 2
Direction 3
Subaru-SCExAO？

## Slide 21: Future works: until the next WS
Directions １,３
  Simulate Keck NGSAO-like, Gemini GEMS-like instruments
    The expected performance can be confirmed ?
    How shorter wavelength range can we reach ?
Direction２
  Simulate trade-off between SR and size of FoV.
Next round, which direction is the most attractive scientifically ? Which one do you want ?
Do we need next generation general-purpose AO ? Small-scale grade up (SCeXAO, IRWFS etc) or engineering (RAVEN) are not sufficient ?

## Slide 22
“Stellar objects” ： TMT: 1.0”/sample or 0.05”/sample vs. JWST 0.2”/sample @ K-band
Imaging SN10/1hour
Spectroscopy R=1000 SN10/1hour
Sensitivity : vs. TMT, JWST
TMT+AO
TMT+AO
JWST
JWST
Subaru
Subaru
TMT
TMT
In this spectroscopy limit calculation, OH line fluxes are included.
KAB~22
KAB~26.5