## Slide 1
光ファイバー干渉計技術を用いたすばる用超高角分解能・高ダイナミックレンジ撮像装置について
Extremely High Angular-resolution, High-dynamic range Imaging Instrument with Single-mode fiber interferometric techniques
Takayuki Kotani (ISAS/JAXA)

## Slide 2
Overview
Future instruments to realize very high-contrast, high-angular resolution imaging with/without AO for Subaru
Pupil Remapping:
    A new concept for diffraction-limited, high-contrast imaging in visible to NIR wavelengths
    Aperture masking + single-mode fiber interferometer
OHANA
    Optical/Infrared Interferometer array on Mauna Kea
    Extremely high angular resolution (< mas)
    Combining large AO-equipped telescopes including Subaru with a single-mode fiber

## Slide 3
⇒ Adaptive Optics already realized diffraction limited imaging
Relatively low dynamic range around ～λ/D due to residual Atmospheric turbulences
AO performance is limited in the visible wavelengths
High-Contrast, diffraction-limitted imaging from the ground
  However,
Solution： Aperture Masking＋Single-mode fiber

## Slide 4
Several sub-apertures can be used as the array of small telescopes
Original image can be reconstructed with interferometric techniques
Tuthill, Monnier & Danchi, Nature 1999, 398, 487
0.1 arcsec
WR104 at K-band
  Aperture Masking
≒

## Slide 5
Image reconstruction with Aperture Masking
Telescope (Mask)
Focal Plane
Complex
visibility
measurement
Image reconstruction
(Clean, Maximum Entropy, etc)‏
Interference between each sub-apertures
Sub-aperture size < fried length r0
Exposure time (1 frame) < Coherence time t0
Non-Redundant aperture configuration
Non-Redundant
Redundant

## Slide 6
Limirations of Aperture Masking
Sub-aperture size < fried length r0
1) Wavefront erros inside a sub-aperture cannot be zero
Non-Redundant mask
2) Only small part of a telescope aperture can be used
3) Limited number of baselines
Dynamic range is limited to <1000

## Slide 7
FIRST (Fibered Imager foR Single Telescope)‏
Aperture Masking + Single-mode fiber
Degraded wavefront
Flat wavefront
Redundant array
Non-Redundant array
Single-mode fiber
・Single-mode fiber can filter out atmospheric turbulences
・Re-arrangement of Sub-aperture positions

## Slide 8
Extremely high-contrast, sensitive imaging possible
1. SM fibers remove wavefront errors within each sub-apertures
2. Re-arrangement of sub-apertures non-redundantly leads to a full usage of a telescope aperture
3. Post-data processing can remove piston errors between fibers
Redundant Configuration
+ Corrugated Wavefront
Non-Redundant Configuration
+ Spatially Filtered Wavefront
Single-mode
fibers
Lenslet array
Perrin et al. 2006; Lacour et al. 2006
FIRST (Fibered Imager foR Single Telescope)‏

## Slide 9
Simulation (8m telescope)
8m telescope
λ = 550 nm, Δλ = 90 nm
Star magnitude = 5
Seeing: r0 = 8cm @ 550nm, to = 8 msec
Integration time per frame: 1 msec
104.8
Dynamic range
104
106
105.5
13 min
2.2 hour
0.5 arcsec
0.2 sec
Integ. Time
13 sec
Dynamic range = Photon noise limit
・Hot-Jupiters can be directly detected from the ground!
・Only this technique can achieve extremely high-contrast imaging in the visible wavelengths

## Slide 10
FIRST: Development of a 9-fiber prototype system
9-fiber, single-mode fiber Pupil Remapping System
Operating at the visible wavelength (600-800nm)‏
Spectroscopy (R ~ 100)‏
Observations at the Lick Shane Telescope(3m)
Input telescope Pupil
Lens Array
Single-mode
Fiber
Non-redundant Array
2D-Fiber Array
Silicon V-groove chip

## Slide 11
Image reconstruction in the laboratory
CCD Image
Reconstructed image from visibility measurements
Kotani et al., 2009, Optics Express, 17, 1925
(2 x He-Ne Laser)

## Slide 12
On-sky demonstration successfully completed!
Lick 3m telescope
Interferogram of Vega
600 nm
800 nm
July, 29, 2010
9-fiber system
Spectro-interferometry
600-800nm
Ready to go for a larger telescope
(Subaru… )
λ

## Slide 13
OHANA: Optical Interferometer on Mauna Kea

## Slide 14
OHANA: Optical Interferometer on Mauna Kea
OHANA (Optical Hawaiian Array for Nanoradian Astronomy)
    Optical/Infrared Interferometer array on Mauna Kea
    Combining AO-equipped large telescopes including Subaru with a single-mode fiber
    Extremely high angular resolution (sub mas)
    Project started in 2000 (the international team led by Paris observatory)
    2006: First on-sky fringes at Keck-I and Keck-II in the K-band
≒

## Slide 15
Kishimoto et al. 2009, A&A, 507, L57
Radius of Inner Dust Rim
UV Luminosity
Directly Measured-
Size-Luminosity Relation!
    2011: CFHT – Gemini recombination
    201?: Subaru – Keck
    Design of a fiber injection module for Subaru is ongoing at NAOJ
What can we do with OHANA?
OHANA has a potential of:
  Resolving inner most regions of AGN torus
  Directly measuring an accretion disk size
Futur plan
Measured AGN torus size with Keck-interferometer

## Slide 16
Summary
Pupil Remapping:
High-dynamic range, high-angular resolution imaging can be realized with the single-mode fiber pupil remapping technique in the visible to NIR wavelengths
On-sky demonstration successfully completed at the Lick 3m telescope
Pupil remapping at Subaru: up to 106 dynamic range, 12 mas angular resolution imaging possible
Direct detection of extra-solar planets (Hot-Jupiters) in the visible is possible with Subaru
OHANA:
Extremely high-angular resolution optical interferometer
Resolving inner-most regions of AGN dust torus
R&D is ongoing to realize Subaru-Keck interferometer
Notes: - A single-mode fiber pupil remapping system allows a diffraction-limited, high dynamic range imaging at visible wavelengths
- Development of a 36 element prototype system is underway
- Laboratory experiments succesfully demonstated that complex object visibilities can be measured correctly
- FIRST will be tested at the 1m telescope in Meudon in this fall

## Slide 17
Thanks for your attention!
Takayuki Kotani

## Slide 18
14個の未知数
(5個の複素透過率G＋9個の複素数Visibility)‏
Vk: Object Visibility
Gi: 複素透過率 (位相と入射効率)‏
Input (Redundant)‏
ピストン（位相差）は解くことができる！
15個の観測可能な量 > 14個の未知数
Output (Non-redundant)‏
実際に観測できる量は天体のVisibilityではなく、µ (Mutual coherence factor)‏
Post data processingにより、位相差・入射効率の影響を取り除き、完全にフラットな波面を再構築できる！

## Slide 19
Non-redundant VS Redundant
+
２つの干渉縞を分離できないので、
Visibilityを正確に測定できない
＝低S/N, 低ダイナミックレンジ
Non-redundant
mask
Redundant
mask
FT
FT
?
縞の間隔が等しい２つの干渉縞の重なり
位相・振幅は互いに独立に時間変化する