## Slide 1
中間赤外線装置MIMIZUKU
Takashi MIYATA
Institute of Astronomy, University of Tokyo
S. Sako, T. Nakamura, K. Asano, M. Uchiyama,
T. Onaka, I. Sakon, H. Kataza, and TAO group
MIMIZUKU : Mid-Infrared Multi-field Imager for gaZing at the UnKnown Universe

## Slide 2
TAO
a 6.5m infrared/optical telescope
the highest site in the world (5,640m)
at Atacama desert, Chile
ALMA Site
Mid infrared observations from the ground
TAO project

## Slide 3
SWIMS
MIMIZUKU
 Can be attached to the SUBARU Cassegrain focus
Two instruments are now under development
Mid infrared observations from the ground
Instruments for TAO
Motohara+
100
50
0
1 2 3 4 5 10 20 30 40
wavelength [micron]
Transmittance [%]
Excellent sky condition

## Slide 4
Akari and Spitzer achieved excellent results in a number of astronomical fields
very high sensitivity / wide coverage of the sky
Groundbased observations at mid infrared are still important
high spatial resolution
- monitoring capability
Mid infrared observations from the ground
c.f. COMICS
Mid infrared observations from the ground
de Wit et al. 2009

## Slide 5
Many of MIR objects are variables???
quiescence
outburst
EX Lupi (FU Ori type, T Tauri star)
Abraham+ 2009
amorphous +
crystallized
silicate
amorphous
silicate
✓ T Tau stars, HAeBe
✓ AGB stars, Luminous Blue Variables, WR stars
✓ Comets....
10 20 30 40
10 20 30 40
Wavelength [um]
minimum
maximum
Onaka+ 2002
Mid infrared observations from the ground
Mid infrared observations from the ground

## Slide 6
×Unstable sky condition
×Limited number of (comparison )stars
 Differential photometry cannot be applied.
c.f. optical / NIR wavelengths….
a lot of stars + wide filed of view
 Stars around a target object can be used
as a standard of comparison
Monitoring observations at MIR wavelength are difficult
Ground-based telescopes  accurate monitoring is too difficult
Satellite telescopes  lifetime is so limited
observing time is very competitive
Mid infrared observations from the ground
Accurate monitoring at MIR

## Slide 7
Not many stars in MIR sky
Filed of view of current MIR cameras : not so large (< 1arcmin)
 Only the target object is observed at once.
Schematics of the mid-infrared sky
Mid infrared observations from the ground
Accurate monitoring at MIR

## Slide 8
If we can take two (or more) discrete fields simultaneously.....
Differential photometric method can be applied
 improve precision and reliability dramatically
Mid infrared observations from the ground
Accurate monitoring at MIR

## Slide 9
-- consists of two movable pick-up mirrors and a wedge shape mirror
-- picks up two discrete fields of the sky
-- brings into the instrument field of view
Simultaneous observation of two (or more) stars
Field stacker
視野合成▽鏡
低温光学系に
ピックアップ鏡
ピックアップ鏡
回転テーブル
その上にXステージ
望遠鏡の像（仮想的）
1’x2’
1’x2’
2’x2’

## Slide 10
There are enough number of MIR stars ??
Field of VIew | > 50mJy | > 300mJy
φ25’ | 55% | 51%
φ12.5’ | 48% | 39%
φ5.0’ | 23% | 13%
Fraction of two or more Akari 9um objects in a field
Field of VIew | > 130mJy | > 1000mJy
φ25’ | 50% | 41%
φ12.5’ | 41% | 35%
φ5.0’ | 15% | 0.3%
Fraction of two or more Akari 18um objects in a field
20% of 9um sources
10% of 18um sources
Conceptual studies of the field stacker

## Slide 11
Time (sec)
0
20
40
60
80
100
1
1.1
0.9
1.2
0.8
Normalized Intensity
Time variations of star counts
Source A
Source B
A/B
Simultaneous observation improves the photometric accuracy?
Source A, B
A/B
Frequency (Hz)
0.01
0.05
0.1
0.4
1
10
100
0.1
Power
Power spectra of intensity
MIR images of two or more stars taken by COMICS
✓Variation of the intensity : 10% within 100 sec.
✓ Variations of two stars are synchronized
Simultaneous observations are effective
(at least within 1 arcmin)
Conceptual studies of the field stacker

## Slide 12
The field stacker is also useful for spectroscopic observations.
Simultaneous observation enable us
accurate calibration of the atmospheric absorptions
especially for
Field stacker for spectroscopy
Ozone absorption band
at 10 micron
Q-band or longer wavelength ranges

## Slide 13
High spatial resolution
Wide wavelength coverage
Accurate monitoring
Covers 2-38 micron wavelength region ( over 4 octaves!)
Achieves diffraction limited spatial resolution
with the Field stacker
MIMIZUKU : Key concepts

## Slide 14
Filters
Grisms
Filters
Grisms
Filters
Grisms
InSb 1k
    300K
    20K
Si:As ch.
Si:Sb ch.
InSb ch.
2-6μm
20-38μm
6-25μm
Field Stacker
Fore Optics
Slit
Flip-flop mirror
    5K
Si:As 1k
Si:Sb128
from Telescope
MIMIZUKU : Block diagram

## Slide 15
Reflective optics
 wide wavelength coverage
good performances
Cold Optics (20K)
Field Stacker
Pickup mirror
Pickup mirror
Wedge
Mirror
MIMIZUKU : Optics
Up&
down

## Slide 16
MIMIZUKU : Optics

## Slide 17
Parameters | Values |  |  | Notes
# of channels | 3 (Si:As / Si:Sb / InSb) |  |  | 
Detectors | Si:As 1k x 1k | Si:Sb 128 x 128 | InSb 1k x 1k | 
Wavelength coverage | 6-25um | 20-38um | 2-6um | 
Pixel scale | 0.1”/pix | 0.4”/pix | 0.1”/pix | @SUBARU
Field of view | 2’ x 2’ or 1’x2’ x 2fields | 1’ x 1’ or 0.5’x1’ x 2fields | 2’ x 2’ or 1’x2’ x 2fields | @SUBARU
Filters | 10 filtes (6-25um) | 7 filtes (20-38um) | 13 filtes (2-6um) | 
Spectroscopy | R ~400 @Nband R~400 @Qband | R~50 @30um | R~600 @LMband | w/ grism
Sensitivity (Img.) 1sig1sec | 40mJy @10um 130mJy @20um | (400mJy @30um?) |  | for point sources
Instrument size | 2m x 2m x 2m , ~ 2ton |  |  | 
Others | - A cold chopping unit is installed in fore-optics |  |  | 
MIMIZUKU : Specifications

## Slide 18
FY 2010
2011
2012
2013
2014......
Desgin and Development
Tests @ Mitaka
Observations
@ SUBARU
Observations
@ TAO
MAX38
MIMIZUKU
first light
Atacama 1m telescope
Prototype instrument
Tests
@ Hilo
MIMIZUKU : Schedule
Point source images @ 31um / 37um
(Diffraction rings can be seen)

## Slide 19
MIMIZUKU
Summary
✓ Wide wavelength coverage (2-38μm )
✓ High spatial resolution
✓ Accurate monitoring w/ Field stacker
adds an unique
“Monitoring Capability”
....
develops pioneering technology
supplies human resources

## Slide 22
 | MIMIZUKU | COMICS
Sensitivity | ~40mJy @10um 1s1s | ~30mJy @10um 1s1s
Spatial resolution | diffraction limited | diffraction limited
Filed of view | 120” x 120” or 60”x120”x2filed | ~ 40”x30”
Spectral resolution | R~400 @N-band R~400 @Q-band | R~250/2,500/10,000 @N-band R~2,500/5,000 @Q-band
Monitoring Accuracy | Good (w/ Field Stacker) | ---
MIR performances compared with COMICS
△
○
○
○
○
◎
◎
MIMIZUKU will add an unique function of
MIR monitoring observations to the SUBARU telescope
MIMIZUKU : Specifications
COMICS has advantages of
slightly higher sensitivity ( because MIMIZUKU has warm optics)
med/high resolution spectroscopic capabilities