## Slide 1
LBT- Visible AO
Team:
Tianquan Su - Systems
Patrick Llull - Optics
William Hease - Systems
Emily Kopp - Science
Vernon Dunlap – Manager
Design adaptive optics for visible light, λ=0.8μm, for the Large Binocular
Telescope at Mt Graham AZ

## Slide 2
Atmosphere Mt Graham
G-SCIDAR measurements on Mt Graham, 2006, S.E. Egner, et al
λ= 0.5μm
Seeing = 0.67+/- 0.17 arc-sec
r0 = 0.154 m
θ= 2.71+/- 1.11 arc-sec isoplanatic angle
τ= 3.63 +/- 1.66 msec coherence time
λ = 0.8μm
r0 = 0.246 m
θ = 4.32 arc-sec
τ = 5.8 msec wavefront coherence time
VisAO Time Delay = τ /10 = 580 μsec

## Slide 3
# Actuators LBT-VisAO
N = (D/r0)2
D = 8.22 m unobstructed primary mirror
r0 = 0.246 m
N= [8.22/0.246] 2 = 1116.5
1117 actuators
BOSTON MICROMACHINES Corp: MEMS DM
1020 actuators, Stroke=1.5μm, aperture 9.3mm,
Response Time < 20μsec
Custom Order: 1117 actuators, 10.1mm aperture

## Slide 4
Cascade with LBT Secondary
Required STROKE for VisAO, 3.6 μ m, D=8.22 meters
σ^2=1.03(D/ro)5/3 = 357 rad-sqr
σ = 18.89 rad
STROKE = (3)(8e-7)(18.89)/4 λ = 3.6μm
> MEMS STROKE
Cascading the MEMS with the LBT-AOSec will decrease the MEMS stroke requirement because the LBT-AOSec will correct the Lower Order wavefront errors and leave only the Higher Order errors for the MENS to correct.

## Slide 5
Wavefront Error After LBT-AOSec
LBT-AOSec gives a Strehl Ratio = 0.80 for λ = 1.6 µ m
σ^2= -Ln(0.8) = 0.223 rad-sqr
σ = 0.472 rad error in a 1.6 µ m wavelength
Converting error to meters:
Error (RMS) = (0.472)(1.6e-6)/2 λ =0.121 µ m
Converting error to radians in a 0.8 µ m wave:
σ = 2λ(1.21e-7/8e-7) = 0.950 rad
σ^2 = 0.903 rad-sqr
STROKE required of MEMS: 0.173 – 0.287 µ m
Well within MEMS range of 1.5 µ m

## Slide 6
Performance Calculation
WF error calculation:
Parameter used:
Stroke needed on MEMS:
0.173-0.287μm;
σ=0.950 rad after LBT secondary

## Slide 7
LBT-AOSec Cascaded Delay
The LBT-AOSec mirror response time is 0.7ms.
This requires a delay time greater than the 0.58ms allowed by the visible coherence time.
The solution is to send the Slow component to the LBT-AOSec. This is the average WF slopes of two exposures. The LBT-AOSec will run on its normal 1KHz cycle. The Fast component is sent to the MEMS on a 2KHz cycle.

## Slide 8
LBT AO Optical Train
Notes: <number>

## Slide 9
AO Train Characteristics and Roles
DM must be optically located 15.2cm in front of the focal plane (on-axis)
  Length from secondary to focal plane = 13.731m
  DM size: 10.1mm
Use concave parabolic mirror (f = 15.2cm, d = 10.1mm, KK = -1) to collimate light to tip/tilt mirror
  Arranged this way to avoid intrusion of other telescope’s beam propagation to prime focus
  Only correcting beam from one primary (the light incident on the left)
  Achromatic, aberration-free collimation
LBT secondary serves as the Tip/tilt mirror - offloads most of the wavefront error to allow DM provide remaining stroke.
  Corrects the low frequency (<=1kHz) wavefront aberrations
DM: 10.1mm, 1117 actuators, 1.5 micron stroke
  Highest residual wavefront error needed to be corrected for our application was around .3 microns
  Corrects the high frequency (2kHz) wavefront aberrations
Pyramid wavefront sensor design
  High sensitivity: necessary for visible, narrow-field AO
  WFS commands sent to the DM and tilt mirror
  Motor used to control WFS location to achieve maximum sensitivity
Positive aspheric collimator lens: focus corrected light onto the focal plane
  f = 15.2cm
Notes: <number>

## Slide 10
Pyramid Wave Front Sensor
Visible AO requires a bright, natural guide star.
The pyramid WFS will allow us to use natural guide stars that are 1 magnitude dimmer than other WFSs.
  Other WFSs
  Magnitude 8 stars 42,000
  Pyramid WFS
  Magnitude 9 stars 121,000
Notes: <number>

## Slide 11
Pyramid WFS CCD
G
4 CCD
40x40
1134 pix
1134 pix
1134 pix
1134 pix
Slope Calculator
S= [dI/dxn, dI/yn..]
S =[2268x1]
Wavefront Reconstructor
Φ1117
S
8CCD READ-OUTs
MEMS
1117 actuators
Freq Filter
LBT-AOSec &
Reconst
672
Low
High
High Order Conv
445

## Slide 12
Slope Calculation
1.1 1.2 1.3
2.1 2.2 2.3
3.1 3.2 3.3
4.1 4.2 4.3

## Slide 13
Modified 4-40x40 CCDs 2-Read-Outs Each

## Slide 14
PWFS CCD
The Pyramid WFS CCD will be 4 40x40 pixel e2v CCDs. Each CCD will have 2 Read-Outs. The 8 parallel read-outs will give a total read-time of (40)(20)(0.3 µ s/pixel) = 240 µ s.
The Read-Outs will all be on the right-side so that corresponding sub-apertures are read at the same time on all 4 pupils. This will allow the Slope Calculator to begin early in the Read-Out.
Exposure 310 µ s
SNR~4.0
Quantum Efficiency = 0.85
Gain=2,
Read Noise, NR=9e-

## Slide 15
Delay Times
Exposure 320µs
Read 240 µs
Slope 199 µ s
Filter 27 µ s
Transmission 44 µ s
Reconstructor 27 µ s
Transmission 44 µ s
High Order Conv 27 µ s
Transmission 44 µ s
MEMS Response 20 µ s
Exposure 320 µ s
Read 240 µ s
Slope 199 µ s
580 µ s

## Slide 16
LBT-VisAO Performance
NGS: M(B)<9.6, M(V)<9.394, M(R)<9.275
Strehl FOV z-from zenith
34.0% 2” 0o
31.8 2 20
30.8 5 0 acceptable limit
23.3 10 0 unacceptable